BILCO Type PCM & PDCM single and double leaf access doors incorporate several innovative features which reduce the amount of labor required to cast the door into a concrete vault. To simplify installation on a standard concrete vault form, doors are designed with a 6" (152mm) high frame (other frame depths available) and have no vertical projections below the frame. Doors are constructed of aluminum and feature a peel off covering to protect the door's finish during the pouring process. For more information, please visit our website www.bilco.com or call 1-800-366-6530.

SECTION 083100

FLOOR ACCESS DOORS

(BILCO TYPE PCM, PDCM)

GENERAL

SUMMARY

Work Included:  Provide factory-fabricated floor access doors.

SUBMITTALS

Product Data:  Submit manufacturer’s product data.

Shop Drawings: Submit shop drawings including profiles, accessories, location, adjacent construction interface, and dimensions.

Warranty:  Submit executed copy of manufacturer’s standard warranty.

QUALITY ASSURANCE

Manufacturer:  A minimum of 5 years experience manufacturing similar products.

Installer:  A minimum of 2 years experience installing similar products.

Manufacturer’s Quality System: Registered to ISO 9001 Quality Standards including in-house engineering for product design activities.

DELIVERY, STORAGE AND HANDLING

Deliver products in manufacturer’s original packaging.  Store materials in a dry, protected, well-vented area. Inspect product upon receipt and report damaged material immediately to delivering carrier and note such damage on the carrier’s freight bill of lading.

WARRANTY

Manufacturer’s Warranty:  Provide manufacturer’s standard warranty.  Materials shall be free of defects in material and workmanship for a period of five years from the date of purchase. Should a part fail to function in normal use within this period, manufacturer shall furnish a new part at no charge.

PRODUCTS

MANUFACTURER

Basis-of-Design Manufacturer:  Type PCM, PDCM Floor Access Door by The BILCO Company, P.O. Box 1203, New Haven, CT 06505, 1-800-366-6530, Fax: 1-203-535-1582, Web: www.bilco.com.

PRECAST VAULT DOOR

Furnish and install where indicated on plans vault access door Type [insert PCM or PDCM], size [insert width (_____) x length (_____)].  Length denotes hinge side.  The floor access door shall be [choose: single or double leaf]. The floor access door shall be pre-assembled from the manufacturer.

Performance characteristics:

Cover(s) shall be reinforced to support a minimum live load of 300 psf (1464kg/m2) with a maximum deflection of 1/150th of the span.

Operation of the cover shall be smooth and easy with controlled operation throughout the entire arc of opening and closing.

Frame shall have an overall depth of 6” (152mm) to facilitate ease of installation on a precast concrete vault.

Operation of the cover shall not be affected by temperature.

Cover:  Shall be 1/4” (6mm) diamond pattern.

Channel frame: Shall be 1/4” (6mm) extruded aluminum with a full anchor flange around the perimeter and have a minimum cross-sectional area of 7.5 in2 (48cm2) for proper drainage.  Frame shall have an overall depth of 6” (152mm) (other frame depths also available).

Hinges:  Shall be specifically designed for horizontal installation and shall be through bolted to the cover and frame with tamperproof Type 316 stainless fasteners.

Drain Coupling:  Provide a 1-1/2” (38mm) drain coupling located on the vertical face of the right front corner of the channel frame [note: can be placed at a different location, if specified].

Lifting mechanisms: A stainless steel torsion bar mechanism, acting through cams, shall be provided to achieve easy, controlled operation through the entire arc of opening and to act as a check in retarding the downward motion of the cover when being closed.

A removable exterior turn/lift handle with a spring loaded ball detent shall be provided to open the cover and the latch release shall be protected by a flush, gasketed, removable screw plug.

Hardware

Heavy forged brass hinges, each having a minimum 3/8” (10mm) diameter Type 316 stainless steel pin, shall be provided and shall pivot so the cover does not protrude into the channel frame.

Cover(s) shall be equipped with a rugged hold open arm which automatically locks the cover in the open position.

Hold open arm(s), lock assembly, and hinges shall be zinc plated and chromate sealed.  (For installation in highly corrosive environments, specify these items in Type 316 stainless steel)

A Type 316 stainless steel snap lock with fixed handle shall be mounted on the underside of the cover.

Finishes: Factory finish shall be mill finish aluminum with bituminous coating applied to the exterior of the frame. Manufacturer shall provide a peel off protective covering on the top surface of the door leaf and frame to protect the surface during the installation process.

EXECUTION

EXAMINATION

Examine substrates and openings for compliance with requirements for installation tolerances and other conditions affecting performance. Proceed with installation only after unsatisfactory conditions have been corrected.

INSTALLATION

Install products in strict accordance with manufacturer’s instructions and approved submittals.  Locate units level, plumb, and in proper alignment with adjacent work.

Test units for proper function and adjust until proper operation is achieved.

Repair finishes damaged during installation.

Restore finishes so no evidence remains of corrective work.

ADJUSTING AND CLEANING

Clean exposed surfaces using methods acceptable to the manufacturer which will not damage finish.

END OF SECTION