BILCO Type SEC security series roof hatches are constructed of heavier gauge materials for high security applications such as correctional facilities, banks, embassies and pharmaceutical buildings. Security Series roof hatches can be fabricated for field installation of many leading brands of security locks. Other options include security glazing and gun ports.  For more information, please visit our website www.bilco.com or call 1-800-366-6530.

SECTION 077233

ROOF HATCHES

(BILCO TYPE SEC)

GENERAL

SUMMARY

Work Included:  Provide factory-fabricated roof hatches for ladder access.

SUBMITTALS

Product Data:  Submit manufacturer’s product data.

Shop Drawings: Submit shop drawings including profiles, accessories, location, adjacent construction interface, and dimensions.

Warranty:  Submit executed copy of manufacturer’s standard warranty.

QUALITY ASSURANCE

Manufacturer:  A minimum of 5 years experience manufacturing similar products.

Installer:  A minimum of 2 years experience installing similar products.

Manufacturer’s Quality System: Registered to ISO 9001 Quality Standards including in-house engineering for product design activities.

DELIVERY, STORAGE AND HANDLING

Deliver products in manufacturer’s original packaging. Store materials in a dry, protected, well-vented area. Inspect product upon receipt and report damaged material immediately to delivering carrier and note such damage on the carrier’s freight bill of lading.

WARRANTY

Manufacturer’s Warranty:  Provide manufacturer’s standard warranty.  Materials shall be free of defects in material and workmanship for a period of five years from the date of purchase. Should a part fail to function in normal use within this period, manufacturer shall furnish a new part at no charge.

PRODUCTS

MANUFACTURER

Basis-of-Design Manufacturer:  Type SEC Security Series Roof Hatch by The BILCO Company, P.O. Box 1203, New Haven, CT 06505, 1-800-366-6530, Fax: 1-203-535-1582, Web: www.bilco.com.

ROOF HATCH

Furnish and install where indicated on plans metal roof hatch Type Security Series, size [insert: width (_____) x length (_____) ]. Length denotes hinge side. The roof hatch door shall be single leaf. The roof hatch shall be pre-assembled from the manufacturer.

Performance characteristics:

Cover shall be reinforced to support a minimum live load of 40 psf (195kg/m2) with a maximum deflection of 1/150th of the span or 20 psf (97kg/m2) wind uplift.

Operation of the cover shall be smooth and easy with controlled operation throughout the entire arc of opening and closing.

Operation of the cover shall not be affected by temperature.

Entire hatch shall be weather tight with fully welded corner joints on cover and curb.

Cover: Shall be 3/16" (5mm) [select: steel or aluminum] with formed reinforcing members. Cover shall have a heavy extruded EPDM rubber gasket that is bonded to the cover interior to assure a continuous seal when compressed to the top surface of the curb. Cover shall be factory prepared to receive a security detention lock  [specify manufacturer and model #], supplied and installed by others in the field. When required, specify cover to be equipped with a factory installed 8" x 8" (203mm x 203mm) bullet resistant view window [specify ballistic rating for glazing] mounted in angle frame flush with top surface of the door leaf.

Cover insulation: Shall be fiberglass of 1” (25mm) thickness, fully covered and protected by a metal liner [select: 22 gauge (.8mm) paint bond G-90 galvanized steel or 18 gauge (1mm) aluminum].

Curb: Shall be 12” (305mm) in height and of 3/16" (5mm) [select: steel or aluminum]. The curb shall be formed with a 3-1/2” (89mm) flange with 7/16” (11mm) holes provided for securing to the roof deck. The curb shall be equipped with an integral metal capflashing [select: 14 gauge (1.9mm) G-90 galvanized steel or 11 gauge (2.3mm) aluminum], fully welded at the corners, that features the Bil-Clip® flashing system, including stamped tabs, 6” (153mm) on center, to be bent inward to hold single ply roofing membrane securely in place.

Curb insulation: Shall be rigid, high-density fiberboard of 1” (25mm) thickness on outside of curb.

Lifting mechanisms: Manufacturer shall provide compression spring operators enclosed in telescopic tubes to provide, smooth, easy, and controlled cover operation throughout the entire arc of opening and closing. The upper tube shall be the outer tube to prevent accumulation of moisture, grit, and debris inside the lower tube assembly. The lower tube shall interlock with a flanged support shoe welded to the curb assembly.

Hardware

Heavy duty manganese bronze hinges shall be provided

Cover shall automatically lock in the open position with a rigid hold open arm equipped with a 1” (25mm) diameter red vinyl grip handle to permit easy release for closing.

Type 316 stainless steel compression spring tubes. All hardware shall be zinc plated and chromate sealed. [For installation in corrosive environments, specify Type 316 stainless steel for the following hardware: latch assembly, interior and exterior padlock hasps, guide arm assembly, lifting mechanism bracket, hinges, hinge pins, hold open arm assembly, lock strike, springs, lifting mechanism support shoes, and all fasteners].

Cover hardware shall be bolted into heavy gauge channel reinforcing welded to the underside of the cover and concealed within the insulation space.

Finishes: Factory finish shall be red oxide primed steel.

EXECUTION

EXAMINATION

Examine substrates and openings for compliance with requirements for installation tolerances and other conditions affecting performance.  Proceed with installation only after unsatisfactory conditions have been corrected.

INSTALLATION

Install products in strict accordance with manufacturer’s instructions and approved submittals.  Locate units level, plumb, and in proper alignment with adjacent work.

Test units for proper function and adjust until proper operation is achieved.

Repair finishes damaged during installation.

Restore finishes so no evidence remains of corrective work.

ADJUSTING AND CLEANING

Clean exposed surfaces using methods acceptable to the manufacturer which will not damage finish.

END OF SECTION